## Slide 1: POWER POINT PRESENTATION BY, VISHAL PANDIT PATIL CLASS:-BSC THIRD YEAR SUBJECT :- PHYSICS TOPIC :- NUMBER SYSTEMS

## Slide 2: Unit-1- Number Systems
INTRODUCTION:-
Binary number systems and digital codes are very essential in computers and digital electronics
In this unit we will study different types of number systems such as binary,decimal,octal,hexadecimal,excess-3-code,BCD,GRAY code etc.
Also we will study how to convert these numbers from one form of number system into another i.e. Interconversion of number system.
Also we will study 1’s compliment representation and 2’s compliment representation of numbers.
Then we will study binary arithmetic i.e. addition, subtraction, multiplication and division of binary numbers.
Having the knowledge of “Binary Arithmetic” we can basically understand the working of computers or other digital systems.

## Slide 3: DECIMAL NUMBER SYSTEM:-
Decimal numbers are the numbers that we use in our daily life. This number system has digits used from 0,1,2,3,4,5,6,7,8 and 9 , therefore BASE or RADIX of decimal number system is 10.
Ex:- (534)10 In above example 534 is the number and 10 is the base of the number system used.
How to find Equivalent Weight of a Decimal Digit:- Decimal number system is a “weighted number system” that means each digit or number of the decimal number system have a fixed weightage .
Lets study how to find out the Equivalent Weight of a Decimal Digit . The weightage of Decimal numbers starts from 1, 10 ,100 ,1000….. so on from right to left for whole numbers and for fractional numbers negative powers of 10 from left to right
The point separating fractional and whole part of the numbers is the Decimal Point.

## Slide 4: How to find Equivalent Weight of a Decimal Digit:-
For example :- In the number (432)10,
Right most digit 2 is called as the Least significant bit i.e. L.S.B. having the lowest weightage
And the digit 4 is called as the most significant bit i.e. M.S.B. having the highest weightage.
The Equivalent weight of the above decimal number can be determined as the follow,
4x100=400 3x10=30 2x1=2 i.e. 400+30+2= 432 is the decimal number with its sum values of each digit.

## Slide 5: Binary Numbers System :-
Computer only knows language of Binary Number system therefore, Binary numbers are very essential in computer and digital codes.
All the programming of the computer is done in the form of binary number system.
In Binary numbers only digits 0 and 1 are used. Hence Base or Radix of a binary number is 2.
Largest Binary number which can be formed using given “n” number of binary digits is given by, (2n -1).
Example:- If 4 binary digits are given then Largest binary number formed is , Here n=4, 2 4 -1 = 16-1 = 15.
Hence , by using 4 binary digits a largest binary number 15 can be formed. e.g. (110001)2 is a binary number. Here 2 is the base of the given binary number.
In this given binary number (110001)2 the rightmost digit 1 is having the least weightage called as the least significant bit i.e. L.S.B. and the left most digit 1 is having the highest weightage and called as the most significant bit i.e. M.S.B.
Binary number system is also a weighted number system. i.e. Each digit of a binary number is having a fixed weightage. Weightage of the binary number increases from right to left

## Slide 6: Octal Number System:-
In Octal number system 8 digits are used from 0,1,2,3,4,5,6 and 7
Hence the base of octal numbers is 8.
Each Octal digit is representing a group of three binary digits
Ex:- (267)8
In above example 267 is the octal number
8 is the base of the number system used.
Octal number system is a “weighted number system” that means each digit or number of the Octal number system have a fixed weightage .Lets study how to find out the Equivalent Weight of a Octal Digit .

## Slide 7: Hexadecimal Number System :-
Hexadecimal number system is an Alphanumeric weighted number system.
In hexadecimal number system digits 0,1,2,3,4,5,6,7,8, 9 and alphabets A,B,C,D,E and F are used.
So in total 16 symbols are used to represent a Hexadecimal number.
Hence the base or radix of the Hexadecimal number is 16
The weightage of Hexadecimal numbers starts from right to left for whole numbers and for fractional numbers negative powers of 16 from left to right

## Slide 8: THANK YOU